## Slide 1
CRYPTOGRAPHY & NETWORK SECURITY | PROJECT PROPOSAL
Secure End-to-End Messaging System Using Hybrid Cryptography
Team Members:
Swetha Kadabgaon (348)
Saniyanaz Momin (350)
Khushi (358)
Nidhi Kugunavar (351)

## Slide 2
PROBLEM IDENTIFICATION
Problem Identification: Insecure Message Transmission
PROBLEM STATEMENT
Conventional messaging applications operating across untrusted networks expose communication to eavesdropping, message tampering, unauthorized server access, and replay attacks. When messages are relayed or stored in plaintext at intermediary servers, an attacker or compromised host can access sensitive records or silently alter data without detection.
Intermediary Server Exposure
Centralized relays traditionally terminate transport connections, exposing plaintext messages and credentials in server databases and memory buffers.
Key Exchange Vulnerability
Transmitting symmetric keys directly over networks allows interceptors to obtain keys. Basic unauthenticated DH remains vulnerable to active MITM substitution.
Lack of Independent Integrity
Without cryptographically binding IV, ciphertext, and sequence nonces via MAC, adversaries can alter bits or replay legitimate intercepted commands.

## Slide 3
PROBLEM IDENTIFICATION
Threat Model & Specific Attack Vectors
Attack 1: Eavesdropping / Sniffing
Passive Attack
Adversaries intercept unencrypted network packets (e.g. using packet analyzers like Wireshark) on untrusted LANs/Wi-Fi, reading plaintext messages and sensitive user data.
Attack 2: Message Tampering
Active Attack
An adversary in transit modifies bits in the ciphertext or parameters, attempting to alter transaction amounts, names, or instructions without recipient detection.
Attack 3: Replay Attack
Active Attack
An attacker captures a valid encrypted transaction packet and re-transmits it later, causing unintended duplicate actions (e.g. repeated funds transfer).
Attack 4: Man-in-the-Middle (MITM)
Asymmetric Attack
In unauthenticated Diffie-Hellman, Eve intercepts public value A and replaces it with A', establishing separate shared secrets with both Alice and Bob while impersonating them.

## Slide 4
SYSTEM DESIGN
Proposed System Architecture & Zero-Knowledge Relay
1. Client Layer (Alice & Bob)
End-to-End Cryptographic Boundary
• Generates ephemeral Diffie-Hellman keypairs locally in client memory.
• Computes shared secret and derives symmetric keys via HKDF-SHA256.
• Performs client-side AES-256-CBC encryption and HMAC-SHA256 generation.
• Validates HMAC and decrypts messages strictly on client device.
2. Transport Layer (TLS / HTTPS)
Communication Channel Security
• Encapsulates client-server communication inside TLS 1.3 encrypted tunnels.
• Utilizes X.509 certificates to protect transport links against eavesdropping.
• Provides hop-by-hop transport confidentiality and channel integrity.
3. Server Relay Layer (Flask)
Untrusted Relay & Message Broker
• Coordinates public DH parameters (p, g, A, B) without learning private keys.
• Enforces anti-replay verification (message ID & sequence check).
• Stores & queues ONLY ciphertext, IV, HMAC tag, and timestamp.
• Core Security Invariant: Zero plaintext messages or session keys on server.

## Slide 5
SYSTEM DESIGN
Hybrid Cryptographic Pipeline Specification
Key Exchange (DH)
RFC 3526 MODP-2048
Alice: a, A = g^a mod p
Bob: b, B = g^b mod p
Shared Secret S = g^(ab) mod p
Secret never sent over network.
Key Derivation (HKDF)
HKDF-SHA256 (RFC 5869)
Derives independent keys:
• K_enc = HKDF(S, 'aes-key')
• K_mac = HKDF(S, 'hmac-key')
Separates confidentiality & integrity.
Confidentiality (AES)
AES-256-CBC + PKCS#7
Plaintext encrypted under K_enc.
Fresh 16-byte random IV per message.
Guarantees message confidentiality against intermediaries.
Integrity & Auth (HMAC)
HMAC-SHA256 (Encrypt-then-MAC)
Tag = HMAC(IV || Ciphertext || TS || Seq, K_mac).
Recipient verifies tag before decryption.
Rejects any altered bits.

## Slide 6
SYSTEM DESIGN
Step-by-Step Message Transmission Protocol
Step 1: Ephemeral Handshake
Alice & Bob exchange public values A and B via relay; verify RSA signatures to prevent MITM.
Step 2: Key Derivation
Both compute identical shared secret S = g^(ab) mod p, then derive AES Key (K_enc) and HMAC Key (K_mac).
Step 3: Encrypt-then-MAC
Alice encrypts plaintext with AES-256-CBC (fresh IV), generates timestamp & seq#, computes HMAC-SHA256 tag.
Step 4: Untrusted Relay
Server receives {sender, receiver, IV, Ciphertext, Tag, TS, Seq#}. Server checks replay filter and queues payload.
Step 5: Integrity Verification
Bob recomputes HMAC over received ciphertext & metadata. If tag does NOT match, message is immediately rejected.
Step 6: Plaintext Recovery
Once integrity is confirmed, Bob checks sequence freshness and decrypts ciphertext using AES-256-CBC.

## Slide 7
SYSTEM DESIGN
Design Mapping: Attacks vs Proposed Defenses
Attack Vector | Vulnerability Cause | Proposed Cryptographic Defense | Expected Security Guarantee
Eavesdropping | Plaintext transmission over network | Dual-Layer: TLS 1.3 (Transport) + AES-256-CBC (E2EE) | Zero plaintext leakage to network sniffers or relay server
Message Tampering | Adversary alters bits in transit | HMAC-SHA256 with Encrypt-then-MAC & constant-time check | Altered ciphertext causes tag mismatch; discarded before decrypt
Replay Attack | Retransmission of valid intercepted packet | Unique UUID message_id, monotonic seq#, and ISO timestamp | Duplicate packet IDs rejected by server & client filters (HTTP 409)
DH Man-in-the-Middle | Unauthenticated public parameter exchange | RSA-2048 PSS Digital Signatures on public DH parameters | Forged public keys fail signature check; connection aborted
Credential Leaks | Plaintext or reversible password storage | PBKDF2-HMAC-SHA256 (100k rounds) with random 16B salt | Resistant to rainbow table and GPU dictionary attacks

## Slide 8
IMPLEMENTATION PLANNING
Implementation Planning: Work Breakdown Structure
Phase 1: Crypto Engine Design
Core Primitives
• Specification of RFC 3526 MODP-2048 Diffie-Hellman algorithm.
• HKDF-SHA256 key separation logic (AES and HMAC keys).
• AES-256-CBC encryption/decryption module with PKCS#7 padding.
• HMAC-SHA256 generation and constant-time comparison logic.
• RSA-2048 PSS digital signature module for MITM prevention.
Phase 2: Server & Database Design
Backend Architecture
• Relational SQLite schema design (users, dh_sessions, messages).
• Authentication endpoints with PBKDF2-HMAC-SHA256 password hashing.
• Public DH parameter exchange coordination routes.
• Encrypted message queuing and anti-replay filter implementation.
• Zero-plaintext database design verification.
Phase 3: Client & UI Architecture
Client Application
• Client-side cryptographic manager for local key isolation.
• Dual-user communication interface (Alice and Bob simulation).
• Real-time Cryptographic Pipeline Inspector for viva/demo visibility.
• Simulated adversary controls (in-flight tampering injection).

## Slide 9
IMPLEMENTATION PLANNING
Planning: Security Verification & Attack Evaluation Plan
Cryptographic Correctness Plan
Unit Testing Suite
• Verify mathematical agreement of Diffie-Hellman: S_A == S_B.
• Verify HKDF produces two strictly distinct 256-bit symmetric keys.
• Verify AES-256-CBC encryption/decryption round-trip with arbitrary text.
• Verify constant-time HMAC tag generation and verification.
• Verify RSA-2048 signature generation and rejection of forged signatures.
Attack Simulation Evaluation Plan
Vulnerability Testing
• Eavesdropping Test: Compare plaintext HTTP vs TLS+AES payload in network captures.
• Tampering Test: Programmatically alter 1 byte in ciphertext; verify HMAC triggers alert.
• Replay Test: Re-send legitimate packet ID; assert rejection with HTTP 409 Conflict.
• MITM Test: Simulate adversary key substitution; verify RSA signature catches mismatch.
Database Security Audit Plan
Zero-Plaintext Verification
• Query raw SQLite tables during active messaging.
• Assert zero plaintext message characters exist in database columns.
• Confirm server never accesses or holds symmetric encryption keys.

## Slide 10
IMPLEMENTATION PLANNING
Technology Selection
• Language & Backend: Python 3.14 + Flask REST API
• Cryptographic Library: Python cryptography (hazmat) + hashlib & hmac
• Database Layer: SQLite3 (Lightweight, zero-config relational store)
• Transport Security: TLS 1.3 / HTTPS with self-signed X.509 certificates
• User Interface: HTML5, CSS3, Modern JavaScript (Dual-panel simulator)
• Testing Framework: Python unittest (Automated security & crypto suites)